P.O. Box 5205 Youngstown, Ohio  44514		         		          Email: sales@skimtech.com

Phone: (330) 774-5044   Fax: (330) 757-7606	         		          Website: www.skimtech.com

Product Overview

Skimall™ Model AG25 “Mini David” Skimming System

The Model AG25 Oil Skimming System is designed to remove free-floating oils, grease and other material from the surface of water in indoor and outdoor applications where space is limited.  The compact design makes it ideal for “tramp oil” removal from metal cutting machine (CNC machine) coolant reservoirs, central coolant systems, parts washers, waste water treatment oil/water equalization tanks, oil/water separators, and hundreds of other applications.

How The Skimmer Works:

The Model AG25 Oil Skimmer uses a specially formulated ¼” diameter collector tube (TigerTube™) that is sized in length for the application and welded into a continuous loop.  The ¼” TigerTube™ collector tube floats on the surface of water and is driven in a continuous loop by the skimmer.  Oils, fats, and grease cling to the outside surface of the TigerTube™ and are drawn into the skimmer.  The material drawn into the skimmer is scraped off the TigerTube™ by abrasive resistant scrapers (Dureon™ scrapers) and flows into a sludge pan with 1” drain coupling.  The clean side of the TigerTube™ collector tube is then driven back to the surface of the water by the skimmer to remove more material.

Typical Removal Rates:

- Light Oils & Grease - 4 GPH

- Medium Oils & Grease - 9 GPH

- Heavy Oils & Grease - 20 GPH

The Model AG25 Oil Skimming System Is Supplied Complete With:

* Safety guard with integral Dureon™ scrapers & pressure blocks.

* 1/12 HP 115 Volt Single Phase Motor.

* Mounting system with universal coupling for ease of installation.

* Sludge pan with 1.0” drain coupling

* Weight - 35 lbs.

* Dimensions (Length x Width x Height) - 12” x 8” x 9”